Receiver Module & Transmitter module G3 description

- Ear Piece socket; 3.5mm jack socket on receiver/Microphone socket on transmitter

- Aerial

- Red LED to show on & battery condition

- Green LED shows RF signal received level

- Menu button & Set

- Scroll button for menu

- Battery compartment (use only Alkaline batteries)

- Battery cover

- Unlock button

- On/off button. (when in menu can be used as escape/cancel)

- LC Display

- Mute switch (located next to microphone socket on transmitter)

How to set up and operate the  G3 radio sets

- Both the transmitter and receiver must be set to a wave length between 606.000 to 648.00 MHz.

- The RFU preferred channel is 608.000

- To set the transmitter to this frequency follow the procedure given below;

- Open battery cover and switch on using button 10 (on/off)

- Press button 5 (set) to open menu

- Menu displays Squelch, this should be set to Low. If not press button 5 and use button 6 to scroll to low then press button 5 to set.

- Use button 6 and scroll up     to advanced press button 5.

- Display now shows Tune.

- Press button 5, display now highlights the first 3 digits, use button 6 to scroll to 608, press button 5 display now highlights last 3 digits use button 6 to scroll to .000 Press button 5 to set. Display now shows tune and under is 608.000

- Now scroll down      with button 6 to exit advanced.

- Display now shows exit press button 5 to set and exit menu.

- The screen now shows the channel selected.

- Sensitivity setting. Press button 5 to open menu, used button 6 to scroll to sensitivity press button 5 and use button 6 to scroll to -18 or 21 then use button 5 to set.

- In advanced with button 6 scroll down to PILOT press button 5 display should show PLT ON. If it shows PLTOFF use button 6 to scroll  to PLTON, then press button 5

- With button 6 scroll down to EXIT and press button 5 and the screen will show advanced use button 6 to scroll to exit press button 5 to exit menu.

- To set the receiver to the frequency 608.000 follow the procedure given above;

- If the screen on the receiver shows MUTE in the bottom right hand corner the MUTE switch on top of the transmitter is activated, this must be turned off with the button next to the microphone socket.

Notes for reference;

- If the screen shows the battery symbol as only one square when you switch on the sets then change for new batteries. Alkaline batteries should last for about 3 matches of 80 minutes.

- Pilot; it is most important to switch this on in both sets. The pilot from transmitter has a unique setting to prevent interference from other radio sets that are working on the same channel in close proximity to each other. (if you wish to listen in to another set do not use pilot)

- If the squelch is set to Hi the receiving distance is greatly reduced and you will lose the referee voice when he turns away or the distance gets too far.

- If you find that the volume is to high on the receiver enter the menu and go to AF OUT and reset to a lower number +3 or +6.